| Division of Finance and Business Operations |  | Procurement & Strategic Sourcing 5700 Cass Avenue, suite 4200 Detroit, Michigan 48202 (313) 577-3734 FAX (313) 577-3747 |
| --- | --- | --- |

3/18/15

Addendum #2 To

Request for Proposal

For Scott Hall Roof Replacement: Project 612-256214

Minutes of the Pre-bid Conference

Dated March 4, 2015

The Addendum must be acknowledged on your lump sum bid.

NOTE: You must have attended a pre-bid conference in order to be eligible to bid on a particular project.  Receipt of minutes or addenda without being at a pre-bid conference does not qualify your company to bid.

Numerous simple questions and answers were addressed at the pre-bid meeting. Some of the issues were as follows:

- There is a note on Sheet A-1.1 that reads “Along west parapet, repair and replace existing tie backs to screen walls as required.”  Is this referring to the large stack tie backs to the parapet wall?

Answer:  This note applies to the various existing angle supports attached to coping for support of the penthouse items to the east.  The parapet roofing and metal cap must be removed to receive new metal gravelstop (base bid), or coping (alternate), and these existing support items shall need to be removed/ re-secured and flashed into the new work with Roof Manufacturer details.

- Upon thoroughly inspecting the interior of the penthouse during the second walkthrough it appears the existing roof sumps are almost impossible to access.  This would make installing the new drains and piping likely not possible, or extremely outrageously priced.  Secondly, replacing the existing drain bowls may not be possible, and may require drain inserts.

Answer:  Due to time remaining for bids, the roof sump replacement shall be deleted from base bid, along with Alternate 1 supplemental roof sumps.  WSU shall reserve the right to promote this roof drainage replacement and supplemental drainage work with the awarded contractor at a later date and prior to roof replacement.

- During our walk through with the Plumbing Contractor on 3/16/2015 we were told that to Install new Drains and Replace the Existing Drains may require removal of duct work and possibly other equipment.   We were unable to locate two of the three Drains as they were blocked out by the duct work and equipment.   Will there be another meeting for the Plumbers to take more time and see what other contractors may be required to provide the removal and replacement of the duct work, etc.?

Answer:   See item no. 2 above.

- Provide approved Manufacturers for replacement Roof Hatch with guard, Safety Post, and Roof Access Ladder.

Answer:

Extendable Safety Post as indicated on A-2.1: Bilco Ladder Up Safety Post, Model LU-2, or approved equal by owner.

Insulated Roof Hatch with railing and self-closing gate as indicated on A-2.1: Verify hatch size in field.  Bilco Type: S Roof Hatch with Bil-Guard Hatch Rail System Model: RL-S.

Approved Manufactures: Precision Ladders or Acudor Products or as approved by owner.

Metal ladder with cage as indicated on A-2.1

Approved Manufactures: Precision Ladders or Alaco Ladder Co. or as approved by owner.

IMPORTANT- This is an addendum which MUST be acknowledged on your bid form.

We will require two copies each of your lump sum proposals, vendor qualification questionnaire and your bid bond documents.

All questions concerning this project must be emailed to: Robert Kuhn, Sr. Buyer, Procurement & Strategic Sourcing.  Email: ac6243@wayne.edu, and copy Cynthia Branch, Buyer, at ab3577@wayne.edu.  Do not contact either FP&M or the Design Firm directly as this may result in disqualification of your proposal.

Thank you for interest shown in working with Wayne State University.

Robert Kuhn

Sr. Buyer

CC:	Robert Jacobs (Project Manager), Cynthia Branch, Buyer, Attendee list.